Version 1.3.8 Last updated 16th March 2015
This document is released under the GNU Free documentation license version 1.3 (https://www.gnu.org/copyleft/fdl.html)

BamM is a c library, wrapped in python, that parses BAM files.
The code is intended to provide a faster, more stable interface to parsing BAM files than PySam, but doesn't implement all / any of PySam's features.

Do you want all the links that join two contigs in a BAM?

Do you need to get coverage?

 Would you like to just work out the insert size and orientation of some mapped reads?

Then BamM is for you!

For impatient people

1. $ BamM make -d <reference.fna> -c read1.R1.fq.gz read1.R2.fq.gz ...
2. $ BamM parse -c covs.tsv -l links.tsv -i inserts.tsv -b mapping.bam
3. $ BamM extract -g BIN_1.fna -b mapping.bam

*BamM make produces indexed and sorted BAM files which contain only reads that mapped.

# Installation
The BAM parsing is done using c and a few external libraries. This slightly complicates the BamM installation process but fortunately not too much.

## Dependencies

If you're running 'BamM make' or you want to run nosetests after installation you'll need to have BWA and Samtools installed. Installation of these tools is really straightforward. You can find the code and instructions at:

Samtools:	https://github.com/samtools/samtools (BamM is tested against v1.2)
BWA:	https://github.com/lh3/bwa (BamM is tested against v0.7.12)

The two external dependencies of BamM; libcfu (v1.0.3) and htslib (v1.2.1) are bundled with the source. I strongly advise against trying to install libcfu independently but there may be some reasons to use a local install of htslib. The notes below are for installing on Ubuntu but they should be transferable to other *nix systems. Be aware that some users have reported difficulty installing the dependencies (htslib) and BamM on OSX, you may need some sysadmin-fu (or need to find someone with a suitable amount of sysadmin-fu) to get things going properly. I strongly doubt this code will work on a Windows system.

First, you need git, zlib, numpy, a C-compiler and some friends. On Ubuntu this looks like:

    $ sudo apt-get -y install git automake build-essential zlib1g-dev python2.7-numpy

### Installing BamM

Get the latest version from github (BamM is not available on pip):

    $ git clone https://github.com/minillinim/BamM.git

If you are using the bundled htslib and libcfu or if these tools are installed system-wide then installation is very straight forward:

    $ sudo python setup.py install

If you installed one or more of these libraries locally then you need to tell setup.py where they are:

    $ python setup.py install --with-libhts-lib /path/to/htslib
 --with-libhts-inc /path/to/htslib --with-libcfu-inc /path/to/libcfu/include/
 --with-libcfu-lib path/to/libcfu/lib/

Relative paths are OK. You can add the --prefix flag to setup.py to install BamM locally. Once done, don't forget to add BamM to your PYTHONPATH. Also, if htslib and libcfu are in non-standard places and you plan to access the C code, you'll need to mess with your LD_LIBRARY_PATH.

I built the install stack using the default tools on ubuntu 14.04 which includes automake-1.14 . This may cause some issues on other systems that use a different version of automake. If you get an error that looks like:
    automake-1.14 command not found
Then you need to rebuild the installer. This is easy. Just go into the 'c' folder within the BamM folder and type:
    $ ./autogen.sh
This should clear up the aclocal issue.

## Testing your installation

After install you can test your installation using nosetests.

First, make sure pip, nose, bwa and samtools are installed:

    $ sudo aptitude install python-pip
    $ sudo pip install nose

Now test BamM:
    $ cd BamM
    $ nosetests

You *should see output like this

$ nosetests
.............................................
----------------------------------------------------------------------
Ran 45 tests in 4.574s

OK

If you have any errors then you should try fix them now (or they may bite you downstream).
# BamM command line overview

I've wrapped the python in a script / library called BamM.
BamM has 3 modes; 'make', 'parse' and 'extract'. The first option allows you to make BAM files. The second option lets you derive coverage profiles or linking information. The final option lets you extract reads that map to a set(s) of contigs.

## Making BAM files

BamM make
Description:
Map several read sets onto a single reference with one command.

Required arguments:
    -d –database <file.fna>	name of fna file to map reads onto

And at least one of:

    -i --interleaved <interleaved.fa> [<interleaved.fa> ...]	shuffled reads
    -c --coupled <coupled.fa> [<coupled.fa> …] paired files
    -s --single <single.fa> [<single.fa> ...]	singleton read files

Optional arguments:
    -p --prefix	''	prefix to apply to BAM files
    -o --out_folder	'.'	write to this folder
    --index_algorithm	auto	algorithm bwa uses for indexing
    --alignment_algorithm	mem	algorithm bwa uses for alignment
    --extras	''	pass extra arguments to BWA
    -k --keep	False	keep all the database index files etc after
    -K --kept	False	assume the indices already exist, don't re-make
    -f --force	False	force overwrite of index files if they are present
    --output_tam	False	output TAM file instead of BAM file
    -t –threads	1	max number of threads to use
    -m --memory	2GB/thread	maximum memory to use per bwa process
Suffix K/M/G recognized
    --show_commands	False	show all commands made by the wrapper
    --quiet	False	suppress output from the mapper
    --silent	False	suppress all output

Example usage:

    $ BamM make -d my_assembly.fa -i ileaved_1.fastq.gz ileaved_2.fastq.gz -c
 paired_R1.fastq.gz paired_R2.fastq.gz -s unpaired.fastq.gz [-t 20] [-v]

This command will make 4 BAM files by mapping the two interleaved read sets, the one paired read set and the singleton read set onto the reference my_assembly.fa
The code calls BWA and Samtools to produce a set of sorted and indexed BAM files. If you specify -t <threads> then BamM will pass this onto BWA and Samtools.
Use -v to get more verbose output.

NOTE: To save space, the final BAM files contain only mapped reads.
NOTE: Output files are automatically named based on the names of the read files and the database, however you can specify the output directory and a prefix to append to the beginning of all output files.

### Passing extra information to BamM

    $ BamM make -d my_assembly.fa -i ileaved_1.fastq.gz ileaved_2.fastq.gz –extras “mem:-k 25”
    $ BamM make -d my_assembly.fa -i ileaved_1.fastq.gz ileaved_2.fastq.gz –extras “aln:-l 25,sampe:-s -a 100”

The first command will pass the extra argument “-k 25” to bwa mem. The second command will pass the extra arguments “-l 25” to bwa aln and “-s -a 100” to bwa sampe.

WARNING
Values passed using --extras are not checked by BamM. This represents a significant security risk if BamM is being run with elevated privileges. Thus you should NEVER run 'bamm make' as root or some other powerful user, ESPECIALLY if you are providing access to multiple / unknown users.

## Getting information from a collection of BAM files

BamM parse
Description:
BamM parse lets you find the insert size(s) and relative read orientation(s) associated with a collection BAM files, it lets you find paired reads that link contigs together and it also lets you create coverage profiles of individual contigs across multiple BAM files.

Required arguments:
    -b –bamfiles <bamfile> [<bamfile> …]	space separated list of BAM files to parse

Optional arguments:
    -l --links	'' filename to write pairing links to
    -i –inserts	''	filename to write insert distributions to
    -c –coverages	''	filename to write coverage profiles to
    -n –num_types	1	number of insert/orientation types per BAM
    -m --coverage_mode	pmean	how to calculate coverage* (req --coverages)
    -r –cutoff_range	?	used to calculate upper / lower rejection cut
   offs when calculating coverage
  --length	ANY	minimum Q length
  --base_quality	ANY	base quality threshold (Qscore)
  --mapping_quality	ANY	mapping quality threshold
  --max_distance	ANY	maximum allowable edit distance from
   query to reference
  --use_secondary	False	use reads marked with the secondary flag
  --use_supplementary	False	use reads marked with the supplementary flag
  -v, --verbose	False	be verbose
  -t –threads	1	maximum number of threads to use

The 'cutoff_range' variable is used for trimmed mean and outlier mean. This argument takes at most two values. The first is the lower cut off and the second is the upper. If only value is supplied then lower == upper.

Example usage:

### Finding the insert size and relative orientation of paired reads

    $ BamM parse -b file.bam

Produces output like this:

    #file insert stdev orientation supporting
    file.bam 899.7514 14.7167 IN 10000

The IN orientation indicates that this is an Illumina-style paired-end (PE) library with an insert of ~900 bp and a standard deviation of ~15 bp. Illumina-style mate pair (MP) libraries will typically have orientation OUT.

Many MP libraries also have a shadow library which looks like someone added some PE reads to the mix. You can tell BamM to look for more than one insert type by specifying the -n option:

    $ BamM parse -n 2 -b mate_pair_file.bam

Produces output like this:

    #file insert stdev orientation supporting
    mate_pair_file.bam 2524.4540 729.1291 OUT 10000
    mate_pair_file.bam 251.6253 44.7241 IN 10000

Multiple BAM files are separated using spaces. The -n argument is space separated too. By default BamM prints this info to stdout. Use the -i argument to specify a file to write the results to.

    $ BamM parse -b pe_file.bam mp_file.bam -n 1 2 -i inserts.tsv

This command will analyse the reads in pe_file.bam and try to find one insert type and the reads in mp_file.bam and try to find two insert types. The resulting table will be written to the file inserts.tsv.

### Creating a coverage profile from several BAM files

When passed the '-c <filename>' argument, BamM will produce a table of coverage values for each BAM file. This is referred to as a coverage profile.

    $ BamM parse -c coverage.tsv -m <COV_MODE> -b f1.bam f2.bam f3.bam

Produces this output in the file 'coverage.tsv'

    #contig Length f1.bam f2.bam f3.bam
    contig_1 946 103.0000 327.0000 369.0000
    contig_3 1147 130.0000 492.0000 778.0000
    contig_5 1465 228.0000 643.0000 970.0000
    contig_7 168 34.0000 82.0000 102.0000
    contig_9 4045 899.0000 1756.0000 2649.0000

The -t option indicates the maximum number of threads BamM will use. This option speeds up the process but you should only use as may threads as you have BAM files. If you have 6 BAM files then you'll see no improvement when using -t 6, -t 7 or -t 700.

Coverage calculation modes

BamM implements several coverage calculation methods. The user can choose the method using the -m argument.

opmean: Outlier pileup coverage: average of reads overlapping each base, after bases with coverage outside mean +/- 1 standard deviation have been excluded. The number of standard deviation used for the cutoff can be changed with --coverage_range.
pmean: Pileup coverage: average of number of reads overlapping each base
tpmean: Trimmed pileup coverage: average of reads overlapping each base, after bases with in the top and bottom 10% have been excluded. The 10% range can be changed using --coverage_range.
counts: Absolute number of reads mapping
cmean: Like 'counts' except divided by the length of the contig
pmedian: Median pileup coverage: median of number of reads overlapping each base

### Finding reads that link 2 contigs

When passed the '-l <filename>' argument, BamM will find paired reads that link contigs.

    $ BamM parse -l links.tsv -b f1.bam f2.bam f3.bam

Produces this output in the file links.tsv:

    #cid_1 cid_2 len_1 pos_1 rev_1 len_2 pos_2 rev_2 file
    contig_2203 contig_3479 1664 334 0 3873 2866 0 f2.bam
    contig_2203 contig_3479 1664 384 0 3873 2818 0 f2.bam
    contig_2203 contig_3479 1664 383 0 3873 2831 0 f2.bam
    contig_2203 contig_3479 1664 349 0 3873 2864 0 f2.bam
    contig_2203 contig_3479 1664 338 0 3873 2862 0 f2.bam

The first (non-header) line is interpreted like this:
contig_2203 is linked to contig_3479.
The first read is towards the start of contig_2203 (len_1 == 1664, pos_1 == 334) and is in the same orientation as the contig (rev_1 == 0)
The second (paired) read is towards the end of contig_3479 (len_2 == 3873, pos_2 == 2866) and is also in the same orientation as the contig (rev_2 == 0)
The linking information was extracted from file: f2.bam.
The lines following this one describe other links between the two contigs.
NOTE: the -i, -c and -l options are not mutually exclusive and can be run at the same time.

## Extracting reads from BAM files

BamM extract
Description:
Extract reads that map to collections of contigs from a collection of BAM files.

Required arguments:
    -g --groups <group> [<group> ...]	files containing reference names (1 per line) or
contigs file in fasta format
    -b --bamfiles <file> [<file> ... ]	BAM files to parse

Optional arguments:
    -p --prefix	''	prefix to apply to output files
    -o --out_folder	'.'	write to this folder
    --mix_bams	False	use the same file for multiple BAM files
    --mix_groups	False	use the same files for multiple group groups
    --mix_reads	False	use the same files for paired/unpaired reads
    --interleave	False	interleave paired reads in ouput files
    --mapping_quality	0	mapping quality threshold
    --use_secondary	False	use reads marked with the secondary flag
    --use_supplementary	False	use reads marked with the supplementary flag
    --max_distance	1000	maximum edit distance from query to reference
    --no_gzip	False	do not gzip output files
    --headers_only	False	extract only (unique) headers
    -v, --verbose	False	be verbose
    -t --threads	1	maximum number of threads to use

Example usage:

Extract all reads mapping to a particular set of contigs

    $ BamM extract -g group1.file group2.file -b f1.bam f2.bam f3.bam

Will extract all reads from each of the three BAM files that map to the contigs in group1 or group2. The 'group' files can be multiple (gzipped) FASTA (like the fna files you can extract from GroopM) or lists of contig headers (one sequence per line).

Unless specified otherwise, BamM differentiates between paired and unpaired reads (from a mapping and group perspective), reads from different BAM files and reads mapping to contigs in different groups.

Paired reads may not be paired when mapped (only one read maps). Also paired reads may map to different groups / bins, so when they're extracted they are unpaired in a group sense. BamM preserves this (and other) information in the read header.
 The read header has the following format:

>g_<group>;p_<pairing_info>;b_<bamfile>;c_<contig_id>;r_<read_id>

Where:
    <group>	the name of the group / bin file with the contig this read maps to.
    <pairing_info>	describes the pairing information about this read (see below).
    <bamfile>	the name of the BAM file containing this read.
    <contig_id>	the id of the contig the read maps to.
    <read_id>	the id of the read as given in the BAM file.

The pairing information has the following format:

   p_<code>R_<code>M_<code>G;

Where <code> is one of:

P	Paired	N	Not applicable
U	Unpaired	E	Error

For example:

p_PR_PM_PG;	indicates a paired read that is mapped as a pair to contig(s) within
the same group.
p_PR_PM_UG;	indicated a paired read that is mapped as a pair to contig(s) that are
in different groups.
p_PR_UM_NG;	indicates a paired read where only this read was mapped.
p_UR_NM_NG;	indicates an unpaired read.

NOTE: this command can produce A LOT of output files.

# Using BamM as a python library

BamM is intended to be used as a python library in any code that needs to produce coverage profiles or paired read linking information. The dev docs will be more useful than this quick guide (see http://minillinim.github.io/BamM/dev_docs/ ). But it's here to give a taste of what you can do with BamM.

## Calculating coverage profiles, insert types or linking reads

The following snippet shows how to calculate a coverage profile within your code.

# first import it
from BamM.bamParser import BamParser
from bamm.bamFile import BM_coverageType

# choose the type of coverage to calculate and make a parser
cov_type = BM_coverageType(CT.P_MEAN_OUTLIER, 1, 1)
BP = BamParser(cov_type)

# get a list of BAM files and parse them
bam_files = ['file1.bam', 'file2.bam']
BP.parseBams(bam_files,
        doLinks=False,	# set to False for no links
        doCovs=True,	# set to False for no coverages
        threads=2)	# 2 files so use 2 threads
The BamParser has an instance variable called a BamFileInfo (BFI). This object contains all the information that has been derived from the BAM files.

        BP.BFI.numBams	the number of BAMs that were parsed
        BP.BFI.bamFiles	path to the BAM files
        BP.BFI.numContigs	the number of contigs in the BAM files
        BP.BFI.contigLengths	array of contig lengths
        BP.BFI.contigNames	array of contig names
BP.BFI.coverages	matrix of coverage values (numContigs x numBams)
        BP.BFI.links	hash of links (see dev docs for more information)

The BamParser comes with several pre-written print functions:

BP.printBamTypes()	print insert information as detailed above
BP.printCoverages()	print coverage information
BP.printLinks()	print linking read information

All of these functions print to stdout. If you supply a file name then BamM will print the information there.